SPECIAL DOORS				SECTION 08 38 00

PART 1 - GENERAL

1.1	RELATED DOCUMENTS

A.	Drawing and general provisions of the Contract, including General and

Supplementary Conditions and Division 1 Specification Sections, apply to this

Section.

1.2	SUMMARY

A.	This section includes traffic doors and frames

1.3	SUBMITTALS

A.	Product Data:  For each type of door and frame indicated.  Include construction

details relative to materials, individual components and profiles, finishes and fire

ratings (if required) for access doors and frames.

B.	Shop Drawings:  Show fabrication and installation details of traffic doors and

frames.  Include plans, elevations, sections, details and attachments to other

Work.

PART 2 - PRODUCTS

2.1	ACCEPTABLE MANUFACTURERS/PRODUCTS

A.   	Traffic Door Manufacturer:  Subject to compliance with requirements, provide

products of the following:

Chase Doors

10021 Commerce Park Drive

Cincinnati, OH  45246

800-543-4455

2.2	TRAFFIC DOORS AND FRAMES

A.	Flexible Traffic Doors

1.	Model 100 Flexible Airgard Doors

08 38 00 - 1

2.   	Doors shall be constructed of 45 oz. USDA accepted, abrasion-resistant,

vinyl coated nylon material and is complete with vision panels and

hardware.

3. 	Pocket weights are provided at the bottom of each panel and the door

panels are sized to allow 1-1/2" overlap at the center.

4.	Wipers are provided at the top, bottom and on the jamb sides.

5.	The door is available in green only.

6.	Window shall be 30"W x 14"H shatterproof polycarbonate.  All windows

shall be factory installed and sealed.  The exposed surface of the

window shall be recessed a minimum of 1/8" from the face of the door to

protect the surface from abrasion from passing loads.  Window shall be

centered 60" from floor.

7.	Doors shall utilize top mounted gravity-operated hinging system,

complete with 1/2" thick base and 5/8" diameter steel rod arm

8.	Door does not have a lower hinge as it is made to swing out, on open,

from heavy excessive traffic.

9.  	Door is not insulated.

# 2.3	WARRANTY

A.	365 days from the date of installation or 395 days from the date of

shipment, whichever comes first.

2.4	FABRICATION

A.	General:  Provide traffic door assemblies manufactured as integral units ready

for installation.

B.	Material surfaces:  For surfaces exposed to view in the completed Work,

provide materials with smooth, flat surfaces without blemishes.  Do not use

materials with exposed pitting, seam marks, roller marks, rolled trade names or

roughness.

08 38 00-2

PART 3 - EXECUTION

A.	Install special doors complete with necessary hardware and accessories in

accordance with final shop drawings, manufacturer's instructions and as

specified herein.

B.	All assemblies must be installed plumb, level and properly aligned.

C.	Upon completion of installation, lubricate, test and adjust doors to operate

easily, free from warp, twist or distortion.

D.	Coordinate installation of bollards and/or wall stops with architectural drawings.

- END OF SECTION 08 38 00 -

08 38 00 - 3