SPECIAL DOORS			SECTION 08 38 00

PART 1 - GENERAL

1.1	RELATED DOCUMENTS

A.	Drawing and general provisions of the Contract, including General and

Supplementary Conditions and Division 1 Specification Sections, apply to this

Section.

1.2	SUMMARY

A.	This section includes traffic doors and frames

1.3	SUBMITTALS

A.	Product Data:  For each type of door and frame indicated.  Include construction

details relative to materials, individual components and profiles, finishes and fire

ratings (if required) for access doors and frames.

B.	Shop Drawings:  Show fabrication and installation details of traffic doors and

frames.  Include plans, elevations, sections, details and attachments to other

Work.

PART 2 - PRODUCTS

2.1	ACCEPTABLE MANUFACTURERS/PRODUCTS

A.	Traffic Door Manufacturer:  Subject to compliance with requirements, provide

products of the following:

Chase Doors

10021 Commerce Park Drive

Cincinnati, OH  45246

800-543-4455

2.2	TRAFFIC DOORS AND FRAMES

A.	 Model Chase Corrections Corrosion Resistant Gate Door

- Doors shall be constructed of 1/2” thick stress relieved and sanitized high density polyethylene material with round edges. Maximum width of a single panel shall be 48”. Door shall meet industry standards for HDPE material of maximum allowable panel deflection of ¼” per 36”. Architect to select color from the full line of manufacturer’s standard SRP colors [black, metallic gray, white, chocolate brown, cloud gray, red, beige].

08 38 00 – 1

2.	Doors shall utilize the Ultra-Soft Touch™ assisted gravity hinge system which is hidden in the anodized aluminum back spine.  The back spine is riveted to the door panel and includes upper and lower stainless steel hinges.

B.	Door Stops

1.	Optional door stops for single panels shall be constructed with 1/2” thick 		stress relieved and sanitized high density polyethylene. Stops shall be 		used to limit the swing pattern.

C.	Frames:  Tubular Steel by door manufacturer.

2.3	FABRICATION

A.	General:  Provide traffic door assemblies manufactured as integral units ready

for installation.

B.	Metal Surfaces:  For metal surfaces exposed to view in the completed Work,

provide materials with smooth, flat surfaces without blemishes.  Do not use

materials with exposed pitting, seam marks, roller marks, rolled trade names or

roughness.

# 2.4	WARRANTY

A.	365 days from the date of installation or 395 days from the date of

shipment, whichever comes first.

PART 3 - EXECUTION

A.	Install special doors complete with necessary hardware and accessories in

accordance with final shop drawings, manufacturer's instructions and as

specified herein.

B.	All assemblies must be installed plumb, level and properly aligned.

C.	Upon completion of installation, lubricate, test and adjust doors to operate

easily, free from warp, twist or distortion.

D.	Coordinate installation of bollards and/or wall stops with architectural drawings.

- END OF SECTION 08 38 00 -