Cold Storage Doors				Section 08 38 00

Part 1 - General

1.0.1   Scope

Work required under this Section shall include the furnishing of all labor, materials, tools, and equipment necessary to complete all insulated door work as detailed on the drawings and/or as specified herein.

1.0.2   Design

Door panel shall be clad with customer's choice of metal. Door frame and trim shall be constructed of FRP. Door casings and track supports shall be constructed of molded plastic polymer (no cladding required). All hardware and mechanisms shall be protected against corrosion by galvanizing or other approved method. Doors shall be complete with all components required for complete installation. Doors with provisions for locking shall have safety release hardware on opposite side.

1.0.3   Substitutions

This specification is written with Chase Doors as the basis of acceptable performance.

1.0.4   Submittals

In compliance with the specification requirements, submit detailed shop drawings for each door, showing in clear detail all mounting requirements and accessories.

1.0.5   Quality Assurance

Doors shall be installed in accordance with the architect's plans and specifications and the door manufacturer's written instructions, drawings and recommendations. Doors shall carry a limited warranty against insulation failure for a period of 5 years from date of original installation. Door frame, trim, vertical casings and header shall carry a limited warranty against warping and rotting for a period of 5 years.

Part 2 - Product

2.0.1   Material

Provide Chase Doors Horizontal Slide Manually Operating Doors including: FRP frame door panel with a foamed-in-place polyurethane core, vertical casings and header constructed of molded plastic polymer (MPP), heavy duty hardware and tracks with corrosion resistant coating. Door includes high density guide rails with 1/8" thick neoprene rubber seal around the perimeter of the door opening and cloth reinforced neoprene rubber bottom sweep gasket capable of providing a gas tight seal. Door track is heat treated 6061 extruded aluminum. Each door panel is suspended with two heavy duty 1-1/4" wide x 4" diameter polyurethane rollers. Each roller has two sealed ball bearings with a capacity of 700 lbs. per roller attached to 1/2" thick steel hanger brackets. Freezer doors include 115 VAC perimeter and bottom of door heat cables to prevent gaskets from freezing.

Part 3 - Execution

3.0.1   Installation

Doors shall be mounted in full accord with the detailed instructions of the door manufacturer and contract documents. When mounting the door casings and header, the mounting surfaces shall be set true and level without distortion and shall be shimmed and caulked to assure tightness and true fitting, and shall be securely lagged. After the doors are hung, they shall be checked for mechanical and electrical operation and tight and uniform gasket sealing. Installation of pull cord switches, power connections to power operated doors and gasket heaters are the responsibility of the electrical contractor.

3.0.2   Product Delivery, Storage and Handling

Each cold storage door shall be securely crated so as to protect the door from damage during shipment and handling. Door identification number shall be clearly marked on the outside of each crate.

3.0.3  Cleaning and Adjustment

Clean all doors of excess sealant, grease, stains, fingerprints and construction dust prior to final inspection to the satisfaction of the architect/owner. Adjust all doors to smooth, proper operating condition, including proper sealing and lubrication, prior to turnover of facility to owner.