SECTION  08386

DOUBLE ACTING IMPACT TRAFFIC DOOR

[QUANTUM MODEL]

GENERAL NOTES TO SPECIFIER:

THIS SPECIFICATION SECTION HAS BEEN PREPARED TO ASSIST DESIGN PROFESSIONALS IN THE PREPARATION OF PROJECT OR OFFICE MASTER SPECIFICATIONS. IT FOLLOWS GUIDELINES ESTABLISHED BY THE CONSTRUCTION SPECIFICATIONS INSTITUTE, AND THEREFORE MAY BE USED WITH MOST MASTER SPECIFICATION SYSTEMS WITH MINOR EDITING.

EDIT CAREFULLY TO SUIT PROJECT REQUIREMENTS. MODIFY AS NECESSARY AND DELETE ITEMS THAT ARE NOT APPLICABLE. VERIFY THAT REFERENCED SECTION NUMBERS AND TITLES ARE CORRECT. (NUMBERS AND TITLES REFERENCED ARE BASED ON MASTERFORMAT, 1995 EDITION).

THIS SECTION ASSUMES THE PROJECT MANUAL WILL CONTAIN COMPLETE DIVISION 1 DOCUMENTS INCLUDING SECTIONS 01330–SUBMITTAL PROCEDURES, 01620–PRODUCT OPTIONS, 01630–PRODUCT SUBSTITUTION PROCEDURES, 01660–PRODUCT STORAGE AND HANDLING REQUIREMENTS, 01770–CLOSEOUT PROCEDURES, AND 01780–CLOSEOUT SUBMITTALS. CLOSE COORDINATION WITH DIVISION 1 SECTIONS IS REQUIRED. IF THE PROJECT MANUAL DOES NOT CONTAIN THESE SECTIONS, ADDITIONAL INFORMATION SHOULD BE INCLUDED UNDER THE APPROPRIATE ARTICLES.

THIS IS AN OPEN PROPRIETARY SPECIFICATION ALLOWING USERS THE OPTION OF APPROVING OTHER MANUFACTURERS WHICH COMPLY WITH THE CRITERIA SPECIFIED HEREIN.

NOTES TO THE SPECIFIER ARE CONTAINED IN BOXES AND SHOULD BE DELETED FROM FINAL COPY.

OPTIONAL ITEMS REQUIRING SELECTION BY THE SPECIFIER ARE ENCLOSED WITHIN BRACKETS, E.G.: [35] [40] [45]. MAKE APPROPRIATE SELECTIONS AND DELETE OTHERS.

ITEMS REQUIRING ADDITIONAL INFORMATION ARE UNDERLINED BLANK SPACES, E.G.: _____________ .

OPTIONAL PARAGRAPHS ARE SEPARATED BY “OR” WITHIN A BOX, E.G.: OR

PART 1 GENERAL

65535.1	SUMMARY

A.	Section Includes: Double acting, self closing, fully insulated, 1-3/4 inch (44 mm) thick, impact traffic door.

INCLUDE APPROPRIATE SECTION(S) BELOW FOR OPENING FRAMING AND DOOR FRAMES. RECOMMENDED FRAME IS A 6 INCH (152 mm) STEEL CHANNEL WITH A 3/8 INCH (10 mm) WEB (MC6 X 18.0). RUBBAIR EXTRUDED ALUMINUM FRAMES CAN BE SPECIFIED IF DESIRED AND ARE INCLUDED IN THIS SECTION AS AN OPTION.

B.	Related Sections:

INCLUDE APPROPRIATE LANGUAGE BELOW INCLUDING A REFERENCE TO SECTION 01030–ALTERNATES, IF PRODUCTS SPECIFIED IN THIS SECTION ARE SUBJECT TO ANY ALTERNATE BID ITEMS, AND ADD SECTION 01030 TO 1.1 B. OTHERWISE DELETE FOLLOWING PARAGRAPH

C.	Alternates:

65535.2	SUBMITTALS

A.	Reference Section 01330–Submittal Procedures; submit the following items:

1.	Product Data.

2.	Shop Drawings: Show fabrication details and anchorage. Include door elevations, head, jamb and meeting stile details including perimeter air seals.

3.	Samples: Full range of manufacturer’s standard color selections for facing material.

4.	Quality Assurance/Control Submittals:

a.	Manufacturer’s Installation Instructions.

5.	Closeout Submittals:

a.	Cleaning and Maintenance instructions.

b.	Warranty

65535.3	QUALITY ASSURANCE

A.	Qualifications:

1.	Manufacturer Qualifications: Minimum five years experience in producing doors  of the type specified.

65535.4	DELIVERY STORAGE AND HANDLING

A.	Reference Section 01660–Product Storage and Handling Requirements.

B.	Verify doors were shipped in upright position.

1.	Note specific doors shipped in other than upright position on bill of lading and contact manufacturer.

C.	Store in upright position and follow manufacturer’s instructions printed on carton.

65535.5	PROJECT/SITE CONDITIONS

A.	Existing Conditions: Frames installed under other sections shall be level and plumb.

65535.6	WARRANTY

A.	One year against defects in materials and workmanship.

PART 2 PRODUCTS

2.1	MANUFACTURERS

A.	Manufacturer: RubbAir Door–Division of Eckel Industries, Inc.;100 Groton Shirley Rd.; Ayer, MA 01432-1050. Telephone: (800) 966-7822, (978) 772-0480.  Fax: (978) 772-7114.

INSERT NAME, ADDRESS AND PHONE NUMBERS OF LOCAL DISTRIBUTOR BELOW.

1.	Distributor:

B.	Model: Quantum

C.	Substitutions: Reference Section 01630–Product Substitution Procedures.

2.2	DOOR COMPONENTS

A.	Panel Construction: Rotationally molded one-piece shell with an overall thickness of 1 ¾ inch (44 mm) and reinforced to 2 ¼ inch (56 mm) thickness at the spine edge.

B.	Core: High density non-CFC urethane foam. Include full height internal steel shaft foamed in-place and secured to top and bottom mounting brackets for additional reinforcement.

C.	Facings: Minimum 3/16 inch (4.5 mm) thick cross-linked polyethylene, color as selected by architect.

D.	Hardware

1.	Cam: Patented “helix” Helical cam design; [1 ¼” inch (32 mm)] standard rise, fabricated from low-friction delrin polymer.

a.	Swing: 125 x 125 degree swing.

2.	Cam Follower: Roller bearing-less helical cam follower with set screw to adjust door height and position, 6061 T6 Aluminum, black anodized with teflon impregnation per AMS-A-8625A.

3.	Bottom Bearing: Floor/jamb mounted food grade 304 stainless steel jamb guard with integral, low friction, igus bearing.

4.	Top and Bottom Hinge Shaft: 1-5/16 inch (33 mm) diameter, food grade stainless steel, #4 grain finish.

E.	Seals: Less than 5 cfm (.002 m³/s) air infiltration per linear foot of seal per ASHRAE Bulletin 90-75

1.	Jamb and Nose Edge: Replaceable polymer impregnated woven nylon fabric in hollow-loop configuration.

2.	Header: Field installed, adjustable, polymer impregnated woven nylon fabric in hollow-loop configuration.

3.	Hardware Cutouts: 1/16 inch (2 mm) thick neoprene rubber, factory installed; fixed.

18X22 INCH (455X560 mm) WINDOWS ARE STANDARD ON PANELS 36” AND GREATER; 14X22 INCH(355X560 mm) WINDOWS ARE STANDARD ON PANELS LESS THAN 36”.

F.	Window: 1/8inch (3 mm) thick polycarbonate, double glazed and recessed 3/16  inch (5 mm), mechanically fastened.

G.	Cam Shields: [1/16 inch (2 mm) black rubber flap.] [ABS plastic, color to match door facing.]

FOLLOWING ACCESSORIES ARE OPTIONAL. SELECT AS DESIRED AND DELETE OTHERS.

2.3	ACCESSORIES

SELECT BUMPERS FROM STANDARD RUBBAIR SIZES; SHOW SIZE AND LOCATION ON DRAWINGS.

A.	Bumpers: 1/4 (6 mm) inch thick molded polyethylene.

B.	Impact Plates: [12 inch (300 mm)] [24 inch (600 mm)] [36 inch (900 mm)] [48 inch (1.22 m)] high, 1/4 inch high density polyethylene.

C.	Rub Rails: 1 inch (24 mm) x 1 inch (24 mm) x panel width, replaceable vinyl strips mounted to a slotted aluminum track, black.

D.	Pressure and Wind Load Accessories:

1.	Adjustable Spring Compensator.

2.     Non-Adjustable Compression Spring

FOLLOWING LOCKING DEVICE IS STANDARD FOR PADLOCK (NOT SUPPLIED); CONTACT RUBBAIR FOR OTHER OPTIONS.

E.	Locking Device: 1 inch (25 mm) i.d. cast aluminum bushing (2 per leaf) with two 3/16 inch (5 mm) by 30 inch (760 mm) long galvanized proof coil chains.

F.	Transom Flap: 2 ply vinyl, color as selected by Architect.

TRACK PORTS AND MEAT RAIL CUTOUTS, IF REQUIRED, SHOULD BE SHOWN ON DRAWINGS.

2.4	FABRICATION

A.	Shop Assembly: Secure top and bottom mounting brackets to rotationally molded door panel using three 3 inch (75 mm) stainless steel bolts each. Position brackets at top and bottom mortises on panel and align center bolt  to secure through the internal tubular steel shaft. Secure windows and all optional features to door panel using stainless steel and zinc coated fasteners.

2.5	SOURCE QUALITY CONTROL

A.	Fabrication Tolerances: Width and height of each leaf: + 0, -3/16 inch (3 mm).

PART 3 EXECUTION

3.1	EXAMINATION

A.	Examine opening in which door will be installed.

B.	Coordinate with responsible entity to perform corrective work on unsatisfactory conditions.

C.	Commencement of work by installer is acceptance of opening conditions.

3.2	INSTALLATION

A.	Follow manufacturer’s instructions.

B.	[Install frames plumb and level.]

C.	Install door with necessary anchors, hardware and accessories.

[1.	Drill bottom bearing for hold open pin.]

3.3	ADJUSTING

A.	Follow manufacturer’s instructions as required to:

1.	Clean and lubricate operating parts.

2.	Adjust to open and close smoothly and freely without binding.

3.	Check seals for proper fit.

3.4	CLEANING

A.	Clean surfaces soiled by work as recommended by manufacturer.

B.	Remove surplus materials and debris from the site.

END OF SECTION